## Slide 1: Review of Network Technologies

## Slide 2: Outline
Network Topology
Local Area Networks
Network Node Components
Internet TCP/IP Protocols
Transmission Technology

## Slide 3: Network Topology - LAN Topology
Bus
Ring
Star

## Slide 4
A Campus Network
Of LANs

## Slide 5: Network Topology - WAN Topology
Mesh
Tree

## Slide 6: 2. Local Area Network
Type of LANs
  Ethernet
  Fast Ethernet
  Gigabit Ethernet
  Half-duplex Vs Full-duplex
  Switched Ethernet
  VLAN (Virtual LAN)
  Token Ring
  FDDI

## Slide 7: Ethernet
IEEE 802.3 standard
10 Mbps data rate
CSMA/CD
  Carrier Sense Multiple Access with Collision Detection
  Analogy of a hollow pipe
  Back Off Algorithm
Packet Size: 64 ~ 1500 bytes
Segment length and drop cable length

## Slide 8: Ethernet
10Base-T :
10 Mbps, Baseband, Twisted Pair

## Slide 9: Fast Ethernet

## Slide 10: LAN - IEEE 802.x
Network
Data Link
Physical
LLC
MAC
802.1 (HLI)
802.2
802.5
802.3
802.4
HLI: High Level Interface
LLC: Logical Link Control
MAC: Medium Access Control
802.1: HLI
802.2: LLC
802.3: Ethernet
802.4: Token Bus
802.5: Token Ring

## Slide 11: Fast Ethernet
100 Mbps
100Base-T
PMD (Physical Medium Dependent) sublayer – to be consistent with IEEE 802.3
UTP Category 5

## Slide 12: Gigabit Ethernet
IEEE 802.3z
1 Gbps
Packet size: 512 bytes

## Slide 13: Full-Duplex Ethernet
Half-Duplex  Full-Duplex
Coaxial Cables can not support full-duplex.
UTP + Hub with full-duplex support
10Base-T, 100Base-T, 100Base-F
↓
10Base-Tx, 100Base-Tx, 100Base-Fx

## Slide 14: Switched Ethernet
Switched Hub
Multi-Port Bridge
=

## Slide 15: Virtual LAN

## Slide 16: Advantages of VLAN
Performance
Formation of Virtual Workgroups
Simplified Administration
Reduced Cost
Security

## Slide 17: Token Ring
IEEE 802.5

## Slide 18: Dual Ring TR LAN

## Slide 19: Failure Recovery in TR LAN

## Slide 20: FDDI
Fiber Distributed Date Interface
Uses fiber optics medium
Modified token ring protocol
Data rate 100 Mbps
Up to 500 DTEs in a single segments of 100 km without repeaters
Ideal for campus backbone network
Single and dual attached stations (SAS and DAS)
Dual attached stations load share the two rings

## Slide 21: Dual Ring FDDI Network

## Slide 22: LAN Data Rate Race
E’Net
10Mbps
FDDI
100 Mbps
Fast E’Net
100Mbps
ATM
155.52 Mbps
Gbit E’Net
1 Gbps
Duplex
E’nets
ATM
OC-n

## Slide 23: 3. Network Node Components
Hubs
Bridges
Remote bridges
Routers
Gateways
Half bridge / half router
Switches

## Slide 24: Basic Network Nodes
Switch
Bridge
Router
Gateway

## Slide 25: Networked Components

## Slide 26: Hubs
Hub is a platform with multiple ports
Function dependent on what is housed
  LAN  multi-port repeater
  Switched LAN  bridge (switched hub)

## Slide 27: Stacked Hub

## Slide 28: Bridges
Bridge
Local Bridge
Remote Bridge
Simple
Multiport
Multiport
Multi-protocol
Refer to Figure 2.17, page 77

## Slide 29: Bridges
Operates at Layer 2, the data link layer.
Allows networks with different physical signaling, but with compatible data link addressing schemes, to communicate.
Helps reduce traffic on a backbone LAN by filtering any information coming from one segment to another that does not need to be forwarded through the backbone.
A common use for a bridge is to allow users on an Ethernet LAN and a Token Ring LAN to communicate with each other.

## Slide 30: Bridges
Remote Bridges
  Used to connect remote LANs
Transparent Bridges
  Used to connect LANs of the same types
  Use a Spanning Tree Algorithm for routing
    Backward learning
    Routing Table of ports associated with destination addresses
Source Routing Bridges
  Used to network token-ring LANs
  Source is aware of the entire path to the destination.

## Slide 31: Routers
Routers operate at network layer
Routes packets between nodes of similar network protocols
Routing table used to route packets
DLC and Physical layers could be different under the same common network layer protocol

## Slide 32: A Router Configuration

## Slide 33: Gateway
Gateway is router connecting two networks with dissimilar network protocols
Gateway does the protocol conversion at the network layer
Protocol Converter
Protocol converter does the conversion at the application layer

## Slide 34: Gateway Configuration

## Slide 35: Tunneling Using Multiprotocol Routers
Tunneling is transmission of packets (via multiprotocol routers) by encapsulation
In Figure 2.24, packets are encapsulated and transmitted through X.25 network in a serial mode

## Slide 36: Half-Bridge/Half-Router
Half-bridge (half-router) is point-to-point communication
Uses PPP protocol
Helps low-end users to communicate with ISP on dial-up link saving the expense of dedicated link
Router encapsulates packets in PPP frames and puts serial outputs to the bridge, and vice-versa

## Slide 37: Switches
Switches are embedded in bridges and routers
Switched network used in WAN
Two types of switched networks
  Circuit-switched
  Packet-switched
    Datagram service
    Virtual circuit

## Slide 39: 5. Transmission Technology
Transmission Technology
Medium
Mode
Wired
Wireless
LAN
WAN
Digital
Analog
LAN Mobile Satellite

## Slide 40: Transmission Media
Media
Wireline
Transmission
Wireless
Transmission
Electric
Conductors
Optical
Fiber
Twisted
Pair
Coaxial
Cable
Mono-mode
Multi-mode
Radio
Microwave
Satellite
Transmission
Infrared
Laser Links
Thin
Thick
UTP
STP

## Slide 41: Transmission Modes
TDM
Packet
Multiplexing
Cell
Multiplexing